## Slide 1: Chapter 1
Using Drawing Instruments

## Slide 2: The Purposes of Drawing and the Tools of Choice
Drawing and illustrating
  The first step in landscaping design
  Presents a concept
  Provides installation information
  Specifies plant selection, special effects, etc
  Testament to company qualifications
Notes: The design of a landscape can be created in a variety of ways
Design a concept of how the designed landscape will look; will have specific information for people installing the landscape to do so correctly

## Slide 3: The Purposes of Drawing and the Tools of Choice
Drawings can be completed with:
  traditional draftsman instruments
  computerized software design systems
A blend of both technologies is most commonly used today

## Slide 4: The Tools and How They Work
T-Square
  long straightedge
  Representation of property lines, roads and drives, fences, and utility lines
  Used as a base of support for other tools like the triangle and lettering templates
Notes: T-Square can be used with drawing board or drawing table to produce a series of parallel horizontal or vertical lines

## Slide 5: The Tools and How They Work
Drawing pencil
  Wooden: have a graphite core
  Lead Holders: chamber holds replaceable leads
Require a sharpening device
  sandpaper pads and specialized pencil sharpeners

## Slide 6: The Tools and How They Work
Drawing leads
  given H or B ratings
  H represents harder lead; the higher the H rating, the harder the lead
  B rating represents a softer lead; the higher the B rating the softer the lead
Most landscapers work with 2H/3H for basic drawings

## Slide 7: The Tools and How They Work
Technical pens
  Used when ink is preferred over pencil
  Ink provides sharper line definition and a greater permanency
  More difficult to correct errors
  Available in disposable and refillable forms
  Create lines of prescribed widths

## Slide 8: The Tools and How They Work
Lettering guides or templates
  Used to create a stenciled lettering style
  Used with a T-Square to keep letters evenly aligned
  When using ink; the templates have raised edges, which allow them to slide back and forth along the T-Square to avoid smearing letters

## Slide 9: The Tools and How They Work
Ames Lettering Guide
  Used with the T-Square to produce guidelines for hand lettering
  Create lines in varied spacing and letters of varied sizes
  These can be replicated endlessly
  Straightedge sides also allow actual letter creation

## Slide 10: The Tools and How They Work
Triangles
  30-60-90 or 45-90 degree angle combinations
  Used as straightedges or in combination with the T-Square to create lines at consistent 30, 45, 60, or 90 degree angles

## Slide 11: The Tools and How They Work
Compass
  Used to create circles
  Circles serve as the basis for the symbolization of plants, patios, pools and lawn areas
  When drawing circles, the distance between the two legs of the compass should be half the desired diameter of the circle

## Slide 12: The Tools and How They Work
Protractor
  measures an angle
  unit of measurement is known as degree
  the center of the protractor’s base is aligned along the lower line of the angle: the angle is determined by reading up from 0 degrees to the point where the line intersects the protractor

## Slide 13: The Tools and How They Work
Curves
  supports for creation of curvilinear lines
  French curves
  flexible curves can be twisted into any shape
  Both are available in various sizes and lengths

## Slide 14: The Tools and How They Work
Scale
  Used to represent actual dimensions in reduced size
  A triangular shape that provides 6 edges; this allows the drawings to have a precise relationship between the drawn length and actual length

## Slide 15: The Tools and How They Work
Engineer’s scale
  divides the inch into various multiples of 10
Architect’s scale
  permits dimensions to be represented as feet and inches

## Slide 16: The Tools and How They Work
Templates
  available in many styles and sizes
  allows the designer the ability to create a neat, attractive plan

## Slide 17: The Tools and How They Work
Erasers
  Plastic erasers: wear away slowly and are washable
  Kneaded Erasers: soft and pliable, used to lift graphite by placing on the line and pressing down

## Slide 18: The Tools and How They Work
Erasers
  Special Purpose Erasers: removal of inked lines or colored marker.
  Liquid Erasers: used for removing old, dried ink lines

## Slide 19: The Tools and How They Work
Erasure shield
  used when erasing graphite lines made with soft B lead
Drafting powder
  prevents smudging and keeps drawing clean

## Slide 20: The Tools and How They Work
Drafting tape
  low adhesive paper tape used to hold the drawing on the board while the designer works
Transparent mending tape
  used when drawings get torn; can sometimes leave a shadow on the prints

## Slide 21: The Tools and How They Work
Rolling ruler
  a straight edge on a roller
  Creates a series of parallel lines at any angle of choice and can also be used to make circles

## Slide 22: The Tools and How They Work
Rendering tools
  colored pencils and markers
  commonly used when preparing the design for presentation to the client